## Slide 1
TITLE PAGE
SafeRoute AI — Dynamic Fire Evacuation Router
Decentralized Edge Mesh with Real-Time Physical Hazard Mapping & 3D Digital Twin
Problem Statement ID: SIH-2026-SR01 (Dynamic Fire Evacuation Router)
Problem Statement Title: Dynamic Fire Evacuation Router with Real-Time Hazard Mapping
Theme: Smart Life-Safety Infrastructure & Edge AI Systems
PS Category: Hardware & Embedded Software Integration
Team Name / Leads: SafeRoute AI Core Engineering Team
Key Innovations: Sub-300ms Edge Dijkstra • ESP-NOW Mesh • 3-Tier Fail-Safe • 3D EOC Twin
Notes: === SCRIPT / WHAT TO SAY ===
Good day judges. We present SafeRoute AI for Problem Statement ID SIH-2026-SR01: Dynamic Fire Evacuation Router with Real-Time Hazard Mapping. SafeRoute AI replaces passive exit signs with decentralized ESP32 edge micro-routers that compute safest exit paths in under 300 milliseconds without central server dependency.
=== KEY TECHNICAL POINTS ===
• Official SIH Title Page format satisfying all metadata fields.
• Highlight Problem Statement ID, Category, and core engineering pillars.
=== SLIDE TRANSITION ===
Let's detail our proposed solution, prototype, and key innovations.
=== EXPECTED JURY Q&A ===
Q: Is this a software or hardware submission?
A: It is a combined Hardware & Software implementation: ESP32 micro-routers with WS2812B LEDs, paired with a Python simulator and 3D WebGL EOC dashboard.

## Slide 2
PROPOSED SOLUTION
PROPOSED SOLUTION / PROTOTYPE
Decentralized Edge Graph
Each node acts as an OSPF-style physical router running Dijkstra on-device.
Multi-Vector Sensor Fusion
Fuses Temperature (°C), Smoke (PPM), Flame (IR), and Occupancy into dynamic edge weights.
Dynamic Visual Guidance
Drives WS2812B chasing LED strips to direct occupants away from hazards.
HOW IT ADDRESSES THE PROBLEM
Eliminates Static Trap
Recalculates paths instantly when fire blocks an exit, reversing chasing LED direction.
Sub-300ms Reaction Time
Updates visual indicators before occupant panic commits people to danger zones.
Zero Single-Point-of-Failure
Runs 100% autonomously without reliance on central servers or power mains.
INNOVATION & UNIQUENESS
Continuous Exponential Math
Uses exponential cost functions exp(αT+βS), avoiding crude binary thresholds.
Lock-Free FreeRTOS Core
Core 0/1 double-buffering avoids mutex priority inversion on hot routing path.
3-Tier Fail-Safe Hierarchy
Seamlessly transitions from local sensors to neighbor consensus on hardware fault.
Notes: === SCRIPT / WHAT TO SAY ===
Slide 2 presents our proposed solution. SafeRoute AI replaces passive exit signs with decentralized link-state micro-routers. Each node senses multi-vector fire data and recomputes paths in under 300 milliseconds. Our innovation lies in our continuous exponential math formula, lock-free FreeRTOS double-buffering, and 3-tier fail-safe hierarchy.
=== KEY TECHNICAL POINTS ===
• Strictly addresses SIH Slide 2 pointers: Proposed Solution, Problem Solved, Innovation & Uniqueness.
• Highlight sub-300ms latency, continuous exponential cost formula, and lock-free execution.
=== SLIDE TRANSITION ===
Let's now examine our technical approach, technologies used, and system flow.
=== EXPECTED JURY Q&A ===
Q: What makes your algorithm unique compared to standard A*?
A: Standard A* uses static heuristic distances. SafeRoute AI computes dynamic physical hazard weights continuously, combining thermal, particulate, and congestion vectors.

## Slide 3
TECHNICAL APPROACH
TECHNOLOGIES & ARCHITECTURE
Embedded Hardware
ESP32 Dual-Core 240MHz, DHT22 (Temp), MQ-2 (Smoke), IR Flame, WS2812B LEDs, Buzzer.
Firmware Stack
C++17 under PlatformIO / FreeRTOS. Core 1 handles ESP-NOW, Core 0 runs Dijkstra.
Networking Mesh
ESP-NOW 2.4GHz connectionless flooding with 24-byte packet, CRC16, and monotonic seq-nums.
Simulation & Twin
Python digital twin injector tool, FastAPI backend bridge, Three.js 3D WebGL EOC UI.
MATHEMATICAL FORMULA & LED MATRIX
edge_cost = (base_dist · exp(2.2·T_norm + 1.6·S_norm) + 0.5·O_norm·base_dist) · (Flame ? 10⁶ : 1)
🟢 GREEN
Safe shortest path; chasing lights point to exit.
🟡 YELLOW
Rerouted alternate route (Smoke-dominant: S_norm > T_norm).
🔴 PULSING RED
Immediate danger (Active flame OR T_norm ≥ S_norm).
⚪ WHITE STROBE
Shelter-in-place state (All exit costs ≥ 100,000).
Notes: === SCRIPT / WHAT TO SAY ===
Slide 3 outlines our technical approach. Our hardware stack uses dual-core ESP32 microcontrollers reading multi-vector sensors. Firmware is written in C++17 on PlatformIO/FreeRTOS, isolating ESP-NOW mesh reception to Core 1 and Dijkstra routing to Core 0. The physical cost math combines temperature, smoke, occupancy, and flame into an exponential edge weight calibrated via NIST fire datasets. FastLED states dictate visual evacuation guidance.
=== KEY TECHNICAL POINTS ===
• Strictly satisfies SIH Slide 3 pointers: Technologies Used & Implementation Methodology.
• Detail FreeRTOS core split, ESP-NOW 24B wire packet, continuous cost math, and FastLED state matrix.
=== SLIDE TRANSITION ===
Let's evaluate the feasibility, risks, and mitigation strategies of our project.
=== EXPECTED JURY Q&A ===
Q: How do you prevent LED path flickering?
A: We implement a 1500–2000ms hold-down hysteresis timer that prevents non-essential route switching unless flame is detected.

## Slide 4
FEASIBILITY AND VIABILITY
FEASIBILITY ANALYSIS
Hardware Cost ($16-$24)
Commodity ESP32 nodes and standard sensors keep per-node BOM extremely low.
Retrofit Friendly
Installs alongside existing code-mandated static signage without rewiring.
Zero Cloud Cost
Operates 100% autonomously without requiring expensive cloud subscriptions.
POTENTIAL CHALLENGES & RISKS
Sensor Failure / Stuck ADC
Physical sensors can break, short-circuit, or freeze ADC values during fire conditions.
Packet Corruption / Drop
RF interference or fire damage can drop mesh packets or corrupt data payloads.
All Exit Traversal Blocked
Severe flashover can block all available building exit paths simultaneously.
MITIGATION STRATEGIES
3-Tier Fail-Safe Hierarchy
Local variance check detects stuck sensors; automatically defers to Tier 2 Neighbor Consensus.
CRC16 & Monotonic Seq-Num
Validates payload integrity and rejects replayed or corrupted packets live.
Shelter-In-Place State
Detects cost ≥ 100,000, triggering White Strobe LEDs to instruct room sealing.
Notes: === SCRIPT / WHAT TO SAY ===
Slide 4 covers Feasibility and Viability. SafeRoute AI is highly feasible with a hardware cost of $16 to $24 per node, retrofitting easily alongside static exit signs. We identified three primary risks: sensor hardware failure, packet corruption, and total exit blockage. We mitigated all three: first, a 3-tier fail-safe hierarchy; second, CRC16 checksums and sequence numbers; and third, an automatic Shelter-In-Place state when all exits are blocked.
=== KEY TECHNICAL POINTS ===
• Strictly satisfies SIH Slide 4 pointers: Feasibility Analysis, Challenges & Risks, Mitigation Strategies.
• Detail 3-tier fail-safe, CRC16 validation, and Shelter-In-Place trigger.
=== SLIDE TRANSITION ===
Let's inspect our project artifacts, code structure, and live dashboard interfaces.
=== EXPECTED JURY Q&A ===
Q: What happens if a node's local sensor dies completely?
A: The node detects zero sample variance over 30s, flags itself unhealthy, and transitions to Tier 2 (Neighbor Consensus) to compute physical hazard costs.

## Slide 5
ARTIFACTS
FIRMWARE & ALGORITHM CODE
• Modular Repository: firmware/src/ (main, routing, fusion, comms, leds, failsafe).
• On-Device Dijkstra: Non-blocking link-state graph solver running on ESP32 Core 0.
• Double-Buffer Swap: Lock-free atomic pointer swap synchronization.
FIRE INJECTOR SIMULATOR
• Multi-Profile Injector: simulator/injector.py streams smolder & flashover profiles.
• Judge Attack Trigger: Allows judges to trigger flashover on arbitrary zones live.
• Corrupt Packet Generator: Injects malformed CRC payloads to prove live rejection.
3D EOC DIGITAL TWIN
• Three.js WebGL Interface: dashboard/ renders 2D/3D floor grid & exit paths live.
• Async IDW Heatmap: Inverse Distance Weighting interpolates heat/smoke surfaces.
• Node Health Panel: Surfaces sensor fault alerts and consensus state live.
PHYSICAL TESTBENCH
• Hardware Prototypes: ESP32 nodes wired with WS2812B strips, MQ-2, DHT22.
• Wokwi Simulation: Full hardware binary simulation suite under tests/.
• Timing Benchmark Logs: Measured p95 reaction latency of 118ms across 4 hops.
Notes: === SCRIPT / WHAT TO SAY ===
Slide 5 displays our working project artifacts: modular C++ firmware, Python fire simulator supporting judge flashover triggers and CRC corruption tests, 3D WebGL EOC digital twin, and physical testbench benchmarks proving a 118ms p95 latency across 4 hops.
=== KEY TECHNICAL POINTS ===
• Strictly satisfies SIH Slide 5 pointers: Embedded Code, Solution Snaps, Dashboard Snaps, Simulator.
• Highlight physical testbench, Python injector, and Three.js 3D Digital Twin.
=== SLIDE TRANSITION ===
Let's conclude with our research references and dataset calibrations.
=== EXPECTED JURY Q&A ===
Q: Is the code open source and available for review?
A: Yes, the full repository includes firmware source code, Python digital twin injector, Node-RED flows, tests, and Docker deployment scripts.

## Slide 6
RESEARCH AND REFERENCES
DATASETS & CURVE REGRESSION
NIST Fire Dynamics Data
Extracted temperature rise timelines and smoke flashover curves from National Institute of Standards and Technology public research.
Kaggle Smoke Datasets
Used public smoke detection time-series data to fit logistic growth curves for smoldering fire profiles.
Hyperparameter Tuning
Offline regression scripts under simulator/fire_profiles/ fit α=2.2 (thermal) and β=1.6 (smoke) parameters.
STANDARDS & TECHNICAL REFERENCES
NFPA 101 Life Safety Code
Framed system to augment — not replace — code-mandated static illuminated exit signage in commercial facilities.
OSPF RFC 2328 Protocol
Applied classical link-state network graph routing concepts to physical hazard topology modeling.
FreeRTOS Dual-Core Architecture
Implemented lock-free double-buffered pointer swapping based on real-time embedded systems literature.
Notes: === SCRIPT / WHAT TO SAY ===
Slide 6 presents our research foundation and references. Our cost function constants α=2.2 and β=1.6 were fitted using offline non-linear regressions on NIST fire dynamics data and Kaggle smoke datasets. SafeRoute AI is designed to augment static signage under NFPA 101 standards, applying classical OSPF link-state graph routing principles to physical fire evacuation. Thank you, and we are open for jury questions.
=== KEY TECHNICAL POINTS ===
• Strictly satisfies SIH Slide 6 pointers: Reference Links & Research Work Details.
• Highlight NIST fire data, Kaggle smoke time-series, NFPA 101 regulatory framing, and OSPF graph theory.
=== SLIDE TRANSITION ===
End of presentation. Open floor for jury Q&A.
=== EXPECTED JURY Q&A ===
Q: How do you justify fitting hyperparameters offline instead of running ML on-device?
A: Safety-critical emergency routing requires deterministic execution. Offline regression calibrates accurate continuous physics curves while ensuring on-device Dijkstra runs in bounded sub-300ms time.